## Slide 1
WATERWATCH
ESP32-Based Smart Overhead Tank Water Quality & Supply Monitor
Presented by: Bhuvanesh Chinnathambi
Electronics and Communication Engineering

## Slide 2
MANUAL RISKS
Manual pump operation leads to dry runs or overflows.
Fixed timers fail to account for variable usage patterns.
Zero real-time water quality monitoring for resident health.
Problems are detected only after someone complains.
THE PROBLEM NOBODY SEES COMING

## Slide 3
SENSE
Continuous monitoring of tank levels and TDS quality signal.
DECIDE
ESP32 filters noise and applies intelligence to start/stop the pump.
CONTROL
Automated relay switching with dry-run protection and solar backup.
MISSION: CONDITION-DRIVEN MANAGEMENT

## Slide 4
THE BIG PICTURE
INTELLIGENT IoT ARCHITECTURE
Renewable Solar Energy Core
Battery-Backed Stability
ESP32 Central Control
Triple Sensor Feedback Loop

## Slide 5
CONTROLLER
ESP32 DevKit V1 (WiFi/BT Embedded)
LEVEL SENSING
HC-SR04 Ultrasonic Sensor
QUALITY
Analog TDS/Quality Potentiometer
POWER
Solar + Charge Controller + Buck Converter
HARDWARE INTELLIGENCE

## Slide 6
ENERGY FLOW
Designed for reliable, 24/7 off-grid monitoring of critical water infrastructure.
•
Solar Module: Daytime generation.
•
12V Battery: Night-time monitoring.
•
Buck Converter: Precise 5V/3.3V for ESP32 logic.
•
Fail-Safe: State retention on power restore.
SOLAR-ASSISTED POWER ARCHITECTURE

## Slide 7
HYSTERESIS CONCEPT
A single threshold causes the pump to "chatter" — rapid ON/OFF switching that burns out relay contacts and motors.
90% STOP
30% START
if (level <= 30) pump = ON;
if (level >= 90) pump = OFF;
WHY 30% ON AND 90% OFF?

## Slide 8
DRY-RUN PROTECTION
The overhead tank cannot detect if the source is empty. Monitoring the underground sump is critical.
"Preventing pump destruction through source-aware logic."
SUMP LEVEL ≤ 20%
Pump operation is immediately blocked. Alarm Triggered.
THE GUARD BENEATH THE TANK

## Slide 9
TANKER FILL EVENT
The system distinguishes between a pump-driven rise and an external tanker fill.
if (Level Increasing && Pump == OFF)
{ Result = TANKER_FILL; }
WHEN THE TANK RISES BY ITSELF

## Slide 10
Signal | ESP32 GPIO
HC-SR04 TRIG | GPIO 5
HC-SR04 ECHO | GPIO 18
Quality Sensor | GPIO 34
Sump Sensor | GPIO 35
Relay Control | GPIO 26
Quality LED | GPIO 27
Buzzer | GPIO 25
*Logic level shifting implemented on Echo pin for ESP32 3.3V safety.
SYSTEM WIRING & INTERFACING

## Slide 11
Monitor the level. Understand the change. Protect the pump. Save the water.
100%
AUTO CONTROL
0
OVERFLOW EVENTS
24/7
QUALITY MONITORING
FINAL IMPACT

## Slide 12
THANKYOU
Any Questions?
Bhuvanesh Chinnathambi
Electronics and Communication Engineering